## Slide 1: Nuclear Medicine Physics
Jerry Allison, Ph.D.
Department of Radiology and Imaging
Medical College of Georgia
Basic Atomic and Nuclear Physics

## Slide 2: Welcome to new residents 2017

## Slide 3: Department of Radiology Medical Physics Resources
Medical Physics Course
  Handouts
http://www.gru.edu/mcg/radiology/residency/resphysicscourse.php

## Slide 4: What to learn?
ABR Core Exam Study Guide
  Physics
    17) Nuclear Medicine and Instrumentation
  Radioisotope Safety Examination (RISE)
https://www.theabr.org/wp-content/uploads/2017/07/CORE_Exam_Study_Guide_FINALV11.pdf

## Slide 5
Nuclear Medicine Physics : A Handbook for Teachers and Students
Diagnostic Radiology Physics: A Handbook for Teachers and Students
International Atomic Energy Agency, 2014
http://www-pub.iaea.org/books/IAEABooks/Subject_Areas/0103/Medical-physics-including-dosimetry-
Wonderful new books (FREE)!

## Slide 6
A note of thanks to
Z. J. Cao, Ph.D.
Medical College of Georgia
And
Sameer Tipnis, Ph.D.
G. Donald Frey, Ph.D.
Medical University of South Carolina
for
Sharing nuclear medicine presentation content

## Slide 7: Electromagnetic wave
Oscillating electric field and perpendicularly oscillating magnetic field which propagate in vacuum at a speed of c = 3 × 108 m/s (~ 1 ft/ns).
  amplitude
  phase
  wave length l
  frequency n
  l.n = c
c

## Slide 8: Spectrum of electromagnetic wave

## Slide 9: Photons
Certain electromagnetic waves such as x-rays and g-rays, can be characterized as quanta or photons.
Photons are like electron and proton particles but with no mass or electric charge.
A photon has energy and momentum.
Photon energy E = h = hc/
Photon momentum p = E/c
  Planck’s constant h = 6.62 x 10-34 J-sec
  Speed of light c = 3 × 108 m/s (vacuum)

## Slide 10: Atomic structure: Bohr model
Atom: the smallest part of an element
size ~ 10-8 cm
mass ~ 1 – 260 u
1 u = 1.66 x 10-27 kg
1 u = 931 MeV (mass of H)
1 u ~ 1 GeV (mass of H)
charge = 0
  Equal numbers of protons and electrons
a nucleus at center and orbital electrons

## Slide 11: Atomic structure: Bohr model
electron charge: -1 or -1.6 x 10-19 Coulomb
electron rest mass: 5.486×10−4 u
  electron mass energy equivalence: 511 keV
nuclear charge: +Z (atomic number)
Pauli exclusion principle:
  electrons allowed for an inner shell ≤ 2n2 (n = 1, 2, 3, …)
  electrons allowed for an outer shell ≤ 8

## Slide 12: Atomic force and energy
electron binding energy
  attractive electric force between the nucleus and electrons
binding energy
  energy needed to free an
  electron a few eV (H) to ~100 keV (U)
  decreases with distance
  from nucleus(outer orbits)
  decreases with smaller
  nuclear charge
E2 = -5 eV
E1 = -10 eV

## Slide 13: Transition of orbital electrons
Inner shell electron vacancies are filled by outer shell electrons, releasing the difference in binding energies
The energy difference
results in
  emission of characteristic
  x-rays, or
  emission of Auger
  electrons

## Slide 14: Characteristic x-rays and Auger electrons
x
-
r
a
y
A
u
g
e
r
e-
15 eV
10 eV
E1
=
-2
0
e
V
E2
=
-5
e
V

## Slide 15: Emission of bremsstrahlung
An incident electron is decelerated and deflected by the nucleus. The energy loss is emitted as bremsstrahlung (braking radiation).
The bremsstrahlung carries energy from 0 up to the full energy of the incident electron.
100 keV e-
bremsstrahlung
x-ray energy (keV)
x-ray intensity
0 25 50 75 100
energy spectrum

## Slide 16: Question
Tungsten has electron binding energies of k = 69 keV, l = 12 keV and m = 2 keV.
If a k shell electron is removed, which emissions could occur?
1. 57 keV characteristic x-ray
2. 10 keV characteristic x-ray
A. 1 only
B. 2 only
C. 1 and 2
C. 1 and 2 is CORRECT

## Slide 17: Question
Consider an atom with electron binding energies of k = 30 keV, l = 4 keV. An Auger electron is ejected from the l shell as following an electron transition from l to k. The energy of the Auger electron is ______ keV.
A. 30
B. 26
C. 22
D. 4
C. 22 is CORRECT

## Slide 18: Nuclear structure
nucleus size ≈ 10-13 cm
nucleus mass: 1 - 230 u
composed of protons and neutrons (nucleons)
mass number A = Z + N
Z: proton number (atomic number)
N: neutron number
A: nucleon number
proton charge: +1
neutron charge: 0

## Slide 19: Nuclear structure
AXZ or X-A e.g. 99Tc43 or Tc-99
isotopes: same Z but different N
1H1 and 2H1, 15O8 and 16O8
isobars: same A but different Z
14C6 and 14N7
isotones: same N (# neutrons) but different Z
3H1 and 4He2
isomers: same A and Z but different energy 99mTc43 and 99Tc43

## Slide 20: Two forces inside nucleus
electric force between protons: repulsive
nuclear force between nucleons: strong and shortly ranged attraction that keeps a nucleus together
The nuclear force produces the binding energy (~ 8 MeV) for a nucleon.
If < 8 MeV, a nucleus is in an excited energy state.
Notes: Electromagnetic force
Strong force
Weak force
Gravitational force
The strong interaction is very strong, but very short-ranged. It acts only over ranges of order 10-13 centimeters and is responsible for holding the nuclei of atoms together. It is basically attractive, but can be effectively repulsive in some circumstances.
The electromagnetic force causes electric and magnetic effects such as the repulsion between like electrical charges or the interaction of bar magnets. It is long-ranged, but much weaker than the strong force. It can be attractive or repulsive, and acts only between pieces of matter carrying electrical charge.
The weak force is responsible for radioactive decay and neutrino interactions. It has a very short range and, as its name indicates, it is very weak.
The gravitational force is weak, but very long ranged. Furthermore, it is always attractive, and acts between any two pieces of matter in the Universe since mass is its source.

## Slide 21: Line of Stability
Naturally occurring (stabile) nuclides
These nuclei have a stable configuration of protons and neutrons in the nucleus
Stable nuclides
  C-12 (6,6)
  O-16 (8,8)
  I-127 (53, 74)
N
Z

## Slide 22: Radionuclides
Many nuclei are not stable (radioactive)
Radionuclides close to line of stability
  Return by beta decay and electron capture
  Radionuclides above the line
    b- (e.g. I-131)
  Radionuclides below the line
    b+ (e.g. F-18) and EC (e.g. Tl-201)
https://commons.wikimedia.org/wiki/File%3ATable_isotopes_en.svg

## Slide 23: Nuclear decay
must obey the conservation laws (energy-mass, electric charge, momentum, etc)
to approach a stable N/Z ratio by
  1. emission of charged particles (, , a)
  2. capture of orbital electrons
  3. fission
to release extra energy by
1. g decay (isomeric transition)
2. internal conversion

## Slide 24: b- decay
A neutron decays to a proton, electron and anti- neutrino: n  p + e- + ~
e- and ~ created inside
the nucleus at the
moment of decay and
ejected right away:
e.g.
99Mo42  99mTc43 + e- + ~
131I53  131Xe54 + e- + ~
e-
~

## Slide 25: b- decay
for neutron rich isotopes
g-ray emission or internal conversion follows if the child nucleus is in an excited state.

## Slide 26: b+ decay
A proton decays to a neutron, positron and neutrino: p  n + e+ + 
e+ and  created in the
nucleus at the moment
of decay and ejected
right away
e.g.
18F9  18O8 + e+ + 
15O8  15N7 + e+ + 
e+


## Slide 27: b+ decay
 decay for proton rich isotopes
g-ray emission or internal conversion follows if the child nucleus is in an excited state.

## Slide 28: Annihilation
e- + e+ => 2 
or
e- + b+ => 2 
each  has energy: 511 keV due to energy-mass conservation or
2 g’s always traveling in opposite directions due to momentum conversation
 PET imaging

## Slide 29: Electron capture
primary: an orbital electron is absorbed into nucleus and is immediately combined with a proton to form a neutron and neutrino:
e- + p  n + 
e.g. 7Be4 + e-  7Li3 + 
secondary: emission of
characteristic x-rays or
Auger electrons
Auger e-

x-ray

## Slide 30: Electron capture
for proton rich nuclei
competing with b+ decay, both produce the same nuclear change of Z to Z-1
probability increasing with larger Z due to closer electron shells

## Slide 31: g decay (isomeric transition)
emitting a g photon to release extra energy of the nucleus: excited state  ground state
99mTc43  99Tc43 + g
g photon ejected
out of the nucleus
g-ray
It often follows other decays that result in an unstable nucleus.
Notes: A metastable state has a half-life greater than 10^-12 seconds
“meta” from the greek means almost --- almost stable

## Slide 32: Internal conversion I.C.
primary: ejection of an orbital electron to release extra energy of the nucleus
no g photons
emitted
secondary:
emission of
x-rays or
Auger e- due to
orbital e- transition
conversion e-
x-ray
Auger e-

## Slide 33: Internal conversion I.C.
competes with g-decay
highest probability for k-shell electrons but other shells possible
It often follows other decays that result in an unstable nucleus.

## Slide 34: a decay
emission of a helium nucleus or a particle
(a: 2 p + 2 n)
226Ra88  222Rn86 + 4He2
235U92  231Th90 + 4He2
occurring for heavy
nuclei
It is often followed
by g-decay or I.C.
a

## Slide 35: Fission
A heavy nucleus breaks into two fragments (usual mass ratio: 40:60).
235U92 + n  92Kr36 + 141Ba56 + 3n + 200 MeV

## Slide 36: Fission
low probability for 235U spontaneous fission (T1/2 = 2×1017y) so neutrons are needed to initiate the fission
Once started, each fission produces more neutrons (1:3) which can sustain fission (chain reaction).
most energy released as heat, also kinetic energies for the fragments and n (~ 1.5 MeV)
controllable in reactor and uncontrolled in atomic bomb

## Slide 37: Nuclear decay rules
Based on conservation laws
-decay and internal conversion: no changes for A & Z
-decay: AXZ  AYZ+1 + e- + ~
-decay: AXZ  AYZ-1 + e+ + 
e-capture: AXZ + e-  AYZ-1 + 
-decay: AXZ  A-4YZ-2 + 

## Slide 38: Nuclear decay scheme
99Mo42  99mTc43 + e- +  (87.6%)
99mTc43  99Tc43 + 
1
4
2
.
7
k
e
V
1
4
0
.
5
k
e
V
0
9
9
T
c
4
3
g
3
g
2
9
9
%
8
9
%
1
%
I
.
C
.
1
1
%
(6.01 h)
9
9
m
T
c
4
3
(2.111x105 y)
g1